# Power board
Current version	r5B12
Status	Completed, ready for production
PCB manufactured	Yes (r5B12)
PCB assembled	Yes (r5B12)
BOM	Yes (Farnell, TME, Digikey, Mouser, RS)
File repository	https://github.com/eez-open/psu-hw/tree/master/Power%20board / (include Eagle, Gerber, BOM files and SPICE simulations)
License	TAPR v1.0
Contributions	C4.1 (Collective Code Construction Contract)
Revision history	2017-03-14: r5B12 / Dual range current programming and measurement (0 – 500 mA, 0 – 5 A) / New current monitor (LTC3050HV) / 16-bit I/O expander / New bias pre-regulator (TL783, LTC3260) / Additional Vin capacitor on Power board (#19) / Rsense with 4-terminal sensing (#21) / Protection improvement for DC power input (#25) / PCB is now 15 mm longer (but still compatible with previous heatsink/mounting holes) / 2016-12-11: r5B11 / Current limiter is removed / 2016-10-24: r5B10 / Added provision for optional components on the AC power input / Voltage programming switch (IC13) wiring fixed (#2) / Main heatsink (Q4) earth connection removed (#3) / Error amps ground reference offset (#11) / 2016-07-24: r5B9 (Version 2.0 on GitHub) / DAC Vdd input moved from digital +5 V to analog +5 V power supply / Changed power input connector type (X1) / Optimized number of parts size and values, renumbered reference designators / 2016-06-16: r5B8 – first public release (successor of pre- and post-regulator boards available in Version 1.0 on GitHub) / SMPS pre-regulator based on LTC3864 / 100% duty-cycle operating mode added for lower output ripple / Optional choice between AC and DC power input / Remote output voltage programming / Remote sense reverse polarity protection / Switching frequency synchronization with other channel via Arduino Shield board (no additional cable required) / On-board SMT temperature sensor (no additional cable required)

Fig. 1: Power board assembled (PCB r5B12, DC power input)
The Power board contains one PSU output channel; two boards are used in the dual channel PSU. This design has at least three distinctive features that make it unusual, or even unique. The first is that the PSU requires a single high voltage input (that can be either DC up to 60 V at the X1 input or AC up to 42 V at the X2 input, see Fig. 2). All required bias voltages are derived from the same source! Therefore no custom made (and costly) transformer (or AC/DC adapter) is required for operation.

Second, it’s a hybrid design and combines the best of two worlds: switching regulation and linear regulation. But the hybrid mode of operation can be changed to linear thanks to the chosen SMPS (Step-Down DC/DC) controller LTC3864. It offers 100% Duty cycle capability which when properly managed with the MCU allows implementing of low ripple mode that will be described below.

Third, its compact design and use of only one 26-pin 0.1” header (X3, see Fig. 12) to carry power output and all control lines simplifies assembly and removes need for several more connecting cables. The only cable remaining is for power input. The Power board is completely portable, and easily replaceable with another (in case of failure), or new one with a different capability and feature set.

The Power board can be divided into the following sections that will simplify its description and understanding:
- Power input
- Power SMPS pre-regulator
- Bias power supply
- Series/pass element, control loops and dual range current
- Output enable (OE) and Down-programmer (DP)
- Digital control (ADC, DAC and 16-bit I/O expander) and voltage reference
- Voltage programming selection
- CC/CV indications
- Remote sense reverse polarity detection
The Power board capability used in the EEZ H24005 model has the following features:
- DC power input (supplied by a Mean Well LRS-150-48 AC/DC module for each channel) which has a maximum output power of 155 W
- Voltage programming: locally (a 16-bit DAC) or remotely/external (+2.5 V for full scale), 0 – 40 V
- Dual range current programming: local (16-bit DAC), 0 – 500 mA, 0 – 5 A
- MCU controlled “Low ripple” mode of operation
For possible modifications and tweaking visit the Hacking area.

## Power input
Fig. 2: Power input and SMPS power pre-regulator
The Power board can be connected to either DC and AC input power using the X1 or X2 connector respectively. AC input can be used when one has a suitable mains transformer available, or if the proposed AC/DC power module is not sufficiently robust. With a properly rated transformer, a maximum output power of 200 W is possible. A potential drawback of using a mains transformer is that its weight will be much more than the AC/DC power modules for the same output power. This will make the hole PSU much heavier and perhaps impractical if it must be moved frequently from one site to another.

The DC input connector (X1) also has a Protective Earth input connected to the capacitors C1 and C2, which are used to reduce improve differential noise. A common-mode choke, L1, was added to suppress noise that appears on the Power board output if it’s supplied from a switching power supply model as recommended.
## Power SMPS pre-regulator
The main role of the power pre-regulator circuit is to efficiently decrease input voltage to the output circuits. If only a linear regulator is used (i.e., for post-regulation) there will be enormous power dissipation when outputting a low output voltage; this will be close to the maximum rated power). A large heatsink, combined with a powerful (and noisy) cooling fan will be needed if the PSU is operated this way, even if using only a single channel in an enclosure compact enough to handle and transport easily. For example, if there is a 48 Vdc input to a power board, and we want to deliver 3.3 V, 5 A at the output, the pass MOSFET (Q4) must dissipate over 220 W to deliver only 16.5 W at the output terminals. This is unacceptable.

Switching regulators, by design, are not operating continuously. By changing their 'on' time at high frequency (and filtering out as much high frequency noise as possible) they can output low voltages more efficiently. The actual efficiency will vary depending on the input and desired output voltages, but 85% and more is easily achievable for high loads (i.e. 1 A and more). This is a considerable improvement and removes the need for very large heat sinks.

If we assume 90% efficiency with a reasonable switching pre-regulator, and that we require about 2 V difference between its output and the final stage (post-regulator) output (such a margin for a maximum load is enough for good regulation), we will have a quite different thermal situation. In the previous example the pre-regulator was required to decrease 48 V to 5.3 V, while dissipating only 21.35 W ((48-5.3 V) x 5 A x (1-0.90)). Losses in the post-regulator will be only about 10 W (2 V x 5 A). The total is about 31.35 W which will be easily manageable with a medium size heatsink, or even a smallish heatsink if a more or less small cooling fan is used.

The LTC3864 (IC1) requires a P-channel MOSFET, which is somewhat unusual choice. The required device characteristics are easier to find in an N-channel device (e.g. low Drain-Source on-state resistance (Rds(on)), high current capability, etc.). In general, P-channel MOSFETs are more expensive, but this design requires only one per channel.

The device selected for MOSFET (Q1), is Infineon’s IRFR5305 which has fairly low Drain-Source on-state resistance Rds(on) reducing its dissipation, and also has modest Input capacitance (Ciss), and Total gate charge (Qg), so there is not much load on the LTC3864’s gate driver.

Another crucial component for a switching regulator is its power inductor (L2). We want up to 5 A, and if we don’t want to occupy much space on the PCB, searching for the proper inductor was rather challenging. Most commercially available power inductors cannot offer more than 33 μH and a rated (Irms) and saturation current (Isat) of at least 5 A. With an inductor with those specifications, it is in principle possible to maintain the regulator’s operation in CCM (Continuous Conduction Mode), for frequencies below 500 kHz.

The LTC3864 provide current monitoring using current shunt resistor (R2) that provides an output current limit (over-current protection) that will be beneficial in case of short circuit.

Synchronization of switching frequency from an external source is done by connecting to the (master) SYNC input that is isolated (pin 16, X3). Synchronization is beneficial in helping suppress undesirable sub-harmonic beat frequencies and in reducing EMI effects.
If multiple SMPS nodes have common ground, sync signal isolation will not be required that is not our case – both channels must be isolated to allow serial or parallel connection, increasing the PSU's flexibility.
Line isolators required to isolate I/O signals for power module controls are not located on the board itself. They are on the Arduino Shield module and they are discussed under Digital isolators.
The “free-running” frequency (without using the sync feature) of the LTC3864 is set via R7 (nominally 47K), and with that value will be slightly less (~300 kHz) then the master SYNC signal (~320 kHz) that comes from the Arduino Shield module. A typical switching waveform is shown on Fig. 3 (measured on Q1's drain with 1 kΩ resistor).

When channel output is switched off, the LTC3864 (using pin 8) is also put into its micropower shutdown state. It only draws about 7 µA.

### Output filtering
Fig. 3: Switching waveform for Vout=20 V, load=16.4 Ω
The main drawback of any switching regulator is the presence at the output noise resulting from the high frequency switching operation. It's often hard to filter out. Low ESR output capacitors will improve the situation to some extent. This PSU does somewhat better by using additional output filtering using L3, L4, C11, C12, and C13. Of course L3 and L4 must be able to handle at least 5 A continuously to provide safe operation.
### Programming output voltage
The pre-regulator's operation is interesting. It’s already been noted that ~2 V difference is about right to keep the post-regulator's power dissipation low (around 10W maximum is about right). A post-regulator output voltage tracking circuit (Q2) is used to do so.

When a fixed output voltage is required the output voltage adjustment is done by using the voltage divider (R13, R16) connected between the pre-regulator’s output (but before final filtering with L3, and L4) and the VFB input (pin 5). That voltage level is continuously compared with the internal reference of 0.8 V. The output voltage can be calculated using the following equation:

Vout = 0.8 V x (1 + R13 / R16)

For example, if we want 5 V at its output with R16 set to 4.7 kΩ, then R13 has to be 24.68 kΩ. If R16 is not installed, the feedback loop build around Q2 should provide an appropriate voltage drop to maintain 0.8 V at the VFB input when the post-regulator output is about 2 V below the pre-regulator's output voltage. If R16 is present, as in our case it must be high enough to program LTC3864’s output above input voltage (48 Vdc in our case) to not interfere too much with the tracker circuit (Q2). With 330 kΩ selected, the output voltage will be about 57 V. Another reason it’s set so high is to ensure that, when the “low-ripple” operational mode is chosen LTC3864 is pushed securely into 100% duty cycle mode.

It’s important to mention that many schematics for a one transistor tracking circuit can be found on the Internet. Most of them may perhaps work well in in theory, or in a Spice simulation. But, because all of them – almost without exception – are missing an important part (C19) they are usually only marginally stable. Without a correctly chosen compensation capacitor, there is likely to be considerable instability under some operational conditions; this may even damage circuit components. The LTC3864 has shown good resilience to such instabilities introduced in the voltage control loop. It gave us enough room to test and find a stability scheme. We are grateful to Dave Jones of the EEVblog for pointing us in the right direction (Video #329).
### Low-ripple mode
Hybrid solutions that combine switching and linear regulators have the advantage when high efficiency and compact design is needed. A switching mode regulator is definitely a better choice if there is a substantial difference between the input and output voltages in the regulator. The main reason for using a linear regulator in the final stage is a better dynamic (i.e. load transient) response and better stability over a wider range of output voltages and currents. There is also an additional noise attenuation effect from a linear regulator final stage. But it such designs can be tricky. Even with an excellent linear regulation final stage, a less than ideal PCB layout will defeat the noise filtering effect and could even introduce instabilities. Using only a two layer PCB instead of multiple layers (4 or more) PCB might not allow good enough performance. We chose a two layer PCB, largely because of the lower cost.

Measuring output ripple and noise is thought by many to be a black art. It seems that many manufacturers publish only results that look better without wasting time on less than spectacular specification and performance details. Even measurement techniques (e.g. using additional capacitors at the output in parallel with the load, favorable choices in output voltages and currents reported, etc.). Generally speaking, only a measuring bandwidth of 20 MHz is mentioned.

The results of measurements taken for this PSU, and the methods used to acquire them, are reported in Measurements. They are more than adequate and compare favorably with high quality, and much more expensive, commercial units. The same is true for output ripple and noise. An example of the standard PSU's ripple and noise with a 16.4 Ω load is given in Fig. 4.

Thanks to the LTC3864's performance, working in the low ripple mode, it’s possible to reduce output ripple and noise figures still further at the expense of voltage and current capacity. For example, with the same load connected as above when the output voltage is decreased to 0.5 V the PSU will enter low ripple mode of operation, cutting noise and ripple in half (Fig. 5).
Fig. 4: Standard output ripple and noise (Iout=0.48 A, Vout=8 V, custom x1 AC probe)

The low ripple mode of operation must be managed by the MCU to limit maximum power dissipation of Q4. It is possible to change the maximum power dissipation limit in firmware, but it should not exceed 30 W for low ripple (Q1 operating in saturation). The worst case, dual channel operation is 60 W. This is established in part by the thermal cooling capacity in the enclosure.
Fig. 5: Low output ripple and noise (Iout=0.45 A, Vout=7.5 V, custom x1 AC probe)
## Bias power supply
The bias power supply (Fig. 6) has two stages: a high voltage LDO (IC3) and low voltage LDO’s for final regulation. The high voltage LDO is selected because the total required bias power is small; the TL783 (IC3) that is used comes in D2PAK package can easily dissipate about 1.5 W when decreasing 48 V down to about 12 V.
LTC3260 (IC4), an inverting charge pump, is used to provide symmetrical low noise regulated outputs of +5 V and -5 V for the linear circuits. It has also the negative voltage output (VOUT, pin 6) required for reliable down-programmer (see below) activation.

The digital section has its own power rail provided by an LP2951 which was selected in part because of its “Power good” indication (ERROR output, pin 5) that can be used for checking power lines “health”. The MCU will not enable power output during start up until that signal is low. Also, if this signal becomes low during normal operation, the firmware will execute a routine which will force the PSU into standby mode.

## Series/pass element and control loops
Fig. 6: Bias power supply (high voltage LDO, Inverting Charge Pump, PWRGOOD signal)
The analog (or central) section of the post-regulator stage is inspired by the exceptional work of Leonid Ivanovitch which was published on of the EEVblog forum.
The N-channel MOSFET (Q4) connected as common drain is used as series regulator. It operate continuously in linear mode when channel is enabled. Therefore SOA is the key design criteria. Thermal design is most important and MOSFETs with low ZthJC (junction-to -case transient thermal impedance) are most suitable.
Q4 requires a bias voltage for normal operation; this is applied on the MOSFET's gate so that it is a few volts above the drain voltage. Commonly for that purpose an additional bias power source derived from an auxiliary secondary transformer winding, or a charge pump gets chosen. The output of such a power source floats on top of the drain voltage since its negative output is connected to the drain voltage, ensuring constant difference between the gate and drain voltages regardless of the input voltage at the drain. Instead of a dedicated gate bias supply, this PSU design uses input voltage. The input voltage has to be e.g. 5 V or more above the maximum output voltage. That requirement is met with Vin at 48 V for 0 – 40 V range.

The zener diode ZD2 ensures the gate-source voltage (Vgs) stays within allowed limits (i.e. below 13 V).

Diode D3 protects Q6 from Base-emitter junction breakdown, and D4 (the same as with D6) was added to prevent current flowing from an external source if output is switched off.

the output voltage on Q4 is controlled by two control loops: constant voltage (at IC5) and constant current (using IC6 and IC7). In general, only one can be active at any given time. Diodes D7 and D9 ensure the output signal from one of the control loops does not affect the other loop. Q11 is a common base voltage amplifier stage, and R34, R45||R46 control local negative feedback.

Both control loops use the same precision voltage reference REF5025 (IC9, Fig. 12) in supervising output voltage and current. The voltage reference is +2.5 V. Therefore, the gain in both control loops must be adjusted so that the output range returns a positive value between zero and +2.5 V. That is done by selecting the feedback loop resistors in IC5B and IC7A which are connected as differential amplifiers. For example, if we’d like to have the output voltage in the range from zero to 40 V, IC5B's gain must be 2.5 / 40 = 0.0625 (in effect, the output signal measurement must be attenuated 16 times).

In practice, due to component tolerances, it is likely the highest values (e.g. 40 V) will not be reached, and a few tens of mV below maximum voltage will be the actual limit when the maximum DAC voltage (generated with 0xFFFF code) is applied to the non-inverting input of the IC5A.

The same problem can be expected on the other end of the voltage range; that the minimum DAC voltage (generated with 0x0000 code) will not get the output voltage down to zero, but only to a few tens of mV above zero. This issue is more important, because it requires a negative DAC voltage – not possible with the DAC chip used (IC10, Fig. 12) without adding an additional operational amplifier. Fortunately such “shrinking” of range issue can be easily overridden with two simple changes:
- At the high end, we need to change the gain factor and
- At the low end, move reference ground potential from zero to, say, 50 mV (applied on IC5B and IC7A non-inverting inputs)
Voltage loop gain (IC5B) can be set to, say, 0.060484 with a combination of 7.5 kΩ (for R39, R52) and 124 kΩ (for R43+R44, R53+R54). For the current loop (IC7A) we can change the gain from an “ideal” of 25 (i.e., 5 A on across a 20 mΩ sense resistor gives 100 mV and 2.5 V / 0.1 V = 25) to, say, 24.39. A combination of 2 kΩ (R60, R70) and 82 Ω (R62, R71) will do it.

A new reference ground potential of about 50 mV can be derived from a +2.5 V reference (IC10) by using the voltage divider R27, R31, and buffering it via IC6B. The offset on the lower programmed output values must be taken into account in firmware, however.

Fig. 7: CV and CC control loops, serial MOSFET driver, OE, DP
Output voltage can be “sensed” locally or remotely. In the first case the inputs at X3-22, and X3-21 must be connected to the power output pins (X3-23...26, X3-17...20). In the second case, the connection is done via the load’s input terminals using a separate cable (i.e. Kelvin wiring) connected directly to the load's terminals. The PSU firmware manages this through the signal relay (K_S1, K_S2) located on the Arduino shield. A remote sensing cable can also be shielded, but the cable shield must be connected to an earth protective terminal only on one end to avoid ground loop problems.
### Current sensing and ranges
The output current is measured by the voltage drop across a current sense resistor (R63 or R65), and the current range can be also defined by changing the values of those resistors – higher values will produce a higher voltage drop for the same current, and therefore IC7A's gain can be reduced. We can improve the precision of the measured value, but using too high a value could produce excessive heating in the current sense resistor. The the dissipated power will rise with the square of the current.

It is important to take into account heating of the current sense resistor since it decreases accuracy because its resistance is temperature dependent. Choosing a resistor with a low TCR while keeping dissipation low will be best. The 20 mΩ value chosen, and a maximum current of 5 A, the dissipated power will be 500 mW. Selected R65 with TCR of 75 ppm/oC temperature at maximum current will increase that change of up to -0.36% can be measured.

Output current can be limited and measured using two ranges: LOW (500 mA) and HIGH (5 A). Selecting the current range is done by switching between two current sense resistors (R63 or R65) using MOSFETs Q13 and Q14. The HIGH range MOSFET, Q14, should have an Rds(on) as low as possible to reduce heating which might affect precision regardless of the current sense resistor temperature stability (TCR).

Since voltage and current are programmed separately, any combination of output current and voltage is possible. Which means that a dual channel asymmetric power supply might be built with different Power board capabilities, e.g., two different output ranges (perhaps 0 – 40 V / 5 A and 0 – 30 V / 3.12 A, etc.).
## Output enable (OE) and down-programmer (DP)
The PSU's Output enable control is a two-state circuit which allows emergency shut down if necessary (e.g. the connected load is overheating, perhaps because of erroneously programmed voltage and current levels). The output enable circuit consists of a Q9, Q10 current mirror controlled by Q12 and Q16 (Fig. 12) that regulates the bias voltage at Q4 delivered by Q6.

The down-programmer (DP) circuit is built using Q7, Q5 that are controlled by Q8 and Q15 (Fig. 12). It’s used to improve output voltage fall times (hence the name, down-programmer).

Fall times (from a previously programmed higher voltage output to a newly programmed lower voltage) will be up to an order of magnitude shorter because of this provision. PSUs without such provisions may delay reduction in output voltage because of energy (ie, charge) stored in the PSU's output capacitor; it could actively supply power to a load for some time. As well, capacitance in the loaded device might do the same.

The difference in programmed output (yellow trace) depending on the DP state is shown below. The PSU's output is programmed with steps from 20 to 1.5 V (10 ms on, 50 ms off) and a 450 Ω load. Fig. 8 shows output without, and Fig. 9 with DP circuit activated.

Fig. 8: Output voltage programming with DP off

Fig. 9: Output voltage programming with DP on
The usual practice is for any down-programmer circuit to follow the state of the output enable circuit; it is enabled when output is enabled, and vice versa. The down-programmer circuit on the Power board could be controlled independently if required; its default state is on, therefore the DP control circuit will be disabled when 5 V is applied to its input (DP_DRIVE signal).

Of course, the down-programmer has a finite sinking capability (limited to about 300 mA via R31). This can be seen when a device with a large capacitance (or just a plain capacitor) is connected to the output. Fig. 10 shows this PSU's fall time of 460 ms with 3 300 μF capacitors charged to 40 V.

## Digital control (ADC, DAC and the 8-bit I/O expander); and the voltage reference
Fig. 10: Output voltage fall time from 40 to 0 V with 3 300 μF
The post-regulator is an analog circuit controlled by analog control loops. Any control function that we want to do digitally (e.g., via MCU firmware) will require signal conversion. These three devices are added to support this requirement(see Fig. 12):
- DAC8552, a dual channel 16-bit Digital to Analog Converter (IC10),
- ADS1120, a 15-bit delta-sigma (ΔΣ) Analog to Digital Converter (IC13), and
- MCP23S17, a 16-bit I/O expander (IC8)
IMPORTANT: All digital devices are powered with 5 V, therefore they cannot be directly connected to the Arduino Due (or to any other 3.3 V MCU board). Also if more then one Power board wants to be connected to the single MCU board, their SPI buses must be isolated from each other even if MCU board used is capable of working with 5 V logic levels.

### Digital to analog converter (DAC)
Fig. 11: Voltage reference, I/O expander, ADC and DAC
The DAC device is used to control the voltage and current for the power supply. Using a SPI bus, the MCU communicates with the DAC to program a new voltage at the DAC's outputs (U_SET and I_SET). This device also includes a power-on reset circuit which ensures that the DAC outputs power up at zero-scale, and remain there until an explicit valid write takes place.

The range of voltage the DAC can manage is determined by the voltage at its reference pin (Vref) which is connected to the precision voltage reference of +2.5 V (IC9).

An important parameter determining the DAC speed (and so PSU response times) is settling time which is the elapsed time from input code write until the output arrives at, and remains within a specified error band around, the final value. For this PSU design, it is at most 10 μs. Another issue is the complexity and actuation delay needed to instruct the DAC. For this device, commands are written by sending 24-bits (the first byte is the command/register selection, and the remaining two bytes (i.e. 16-bits) are converted into an analog voltage). The SPI clock frequency used for transferring 24-bit value can be as hight as 30 MHz (!). The DAC's performance provides enough margin to use it efficiently for PSU programming where new output values change in milliseconds (even including the execution time of necessary MCU code).
### Analog to digital converter (ADC)
The ADC is equipped with a four channel input multiplexer, and can manage up to 2 000 samples per second. Its SPI clock is 4.096 MHz (4.5 MHz max). It's used to measure voltage and current control loops levels (U_MON, I_MON), but also DAC outputs (U_SET, I_SET). The ADC used is a 16-bit bipolar device, that gives 15-bit resolution (positive half) of the full scale (the negative half is not fully used; its monitors down-programmer sinking). It also comes with internal +2.048 V voltage reference. Other features aren't used in this PSU.

In contrast to the DAC, the ADC requires bidirectional communication with the MCU. The ADC’s output transfers results of data acquisition at the end of each measurement. For that purpose, the DOUT/DRDY output is connected to the MISO line. That output could be also used to notify the SPI master (MCU) that data acquisition cycle on the selected input (one of four) is done and data are ready. Another possible arrangement is using the dedicated DRDY output as a notification to the MCU. The JP3 jumper uses the DRDY signal to force an MCU interrupt, tough, of course, a polling routine could be used to periodically acquire converted data.
### 16-bit I/O expander
An I/O expander is used to minimize the number of signal lines needed between a Power board and the digital controller (via the Arduino Shield). The expander’s I/O lines are used in the following manner:

#	Direction	I/O name	Active	Description
0	Input	SENSE_ERR	Low	Reverse remote sense polarity detected
1	Output	SET_DP	Low	Enable or disable down programmer circuit
2	Input	CC_ACTIVE	High	CC (constant current) mode of operation is active
3	Input	EXT_PROG	High	Remote output voltage programming source selection
4	Output	SET_100%	Low	100% duty cycle mode control
5	Input	CV_ACTIVE	High	CV (constant voltage) mode of operation is active
6	Input	PWRGOOD	High	Power good input received from the pre-regulator module
7	Output	SET_OE	High	Enable or disable power output
8	Output	CURR_5A	High	Set high current range resistor
9	Output	CURR_500MA	High	Set low current range resistor
10-15	–	–	–	Not used

### Resolution
One of the starting requirements for this project was a resolution of 10 mV and 10 mA and output range of up to 50 V and up to 5 A. Those requirements require that the resolution of the digital devices used in programming and monitoring output voltage and current are 5 000 programming steps (for a 50 V range). Therefore DAC and ADC resolution must be 13-bit or higher to provide 8 192 or more values (12-bit gives as only 4 096 possible combinations).

The DAC and ADC devices selected meet several criteria: interface connections, speed, availability (i.e. no exotic sources) and, of course, cost. The devices chosen for the post-regulator provide decent price/performance for a PSU design with 16-bit programming resolution and 15-bit measuring resolution. Theoretically the following precisions could be achieved:

Range	16-bit programming	15-bit measurement
0 – 30 V	0.457 mV	0.916 mV
0 – 40 V	0.610 mV	1.22 mV
0 – 50 V	0.763 mV	1.53 mV
0 – 3.12 A	0.0476 mA	0.0952 mA
0 – 4.16 A	0.0636 mA	0.127 mA
HIGH: 0 – 5 A	0.0763 mA	0.153 mA
LOW: 0 – 500 mA	7.63 μA	15.3 μA

For the EEZ H24005 model it is realistic to expect 10 mV output voltage programming and measurement resolution and 1 mA (HIGH range), or well below 0.1 mA (LOW range), output current resolution.
## Voltage programming selection
Output voltage programming has already been covered in the discussion of the reference voltage used by the CV control loop. The digital programming is managed by the MCU, so a user can remotely set desired voltage level using SCPI commands to the firmware via the USB or Ethernet interfaces, or locally via the TFT touch-screen display attached to the Arduino Shield.

Additionally, voltage programming can be performed by applying a positive analog signal (+2.5 V for the full scale). The Arduino Shield has a push-in terminal near the channel output binding posts (X12, X14) reserved for just such remote analog programming. Only one reference signal can be used at a time which is managed with an analog multiplexer/switch (IC12). The default setting is internal. Analog programming is faster, but additional care must be taken to stay within the safe working range even though there is protective circuits (IC12 and the TVS diodes ZD7, ZD10 on the Arduino Shield). Since the MCU can monitor the U_SET signal even when analog voltage programming is used, it’s possible to implement at least an over-voltage protection (OVP) that will switch off channel output if the applied control input signal causes unacceptable output voltage.

One of the uses for the analog programming feature is to use the PSU as a tracking pre-regulator while experimenting with another adjustable linear power supply connected to it. In that case, we would like to keep control dissipated power within safe limits because a suitable heatsink might be missing at the experimental phase, or another flaw in design or testing might cause dangerous heating. Another reason is to simply test how well a power supply under test works at some chosen difference between input and output voltages.
## CC/CV indications
When its output is enabled, the PSU can work in one of the following operational modes:
- CV (constant voltage): when the voltage control loop (IC5) is setting the output voltage. This mode is the default for power supplies with series regulator elements.
- CC (constant current): when the current control loop (IC6, IC7) controls output voltages (and so can limit output current), and
- UR (unregulated, i.e. not regulated): when neither the voltage limit not current limit are controlling the PSU's output.
The CC and CV circuits use “window comparators” that require two comparators: detecting lower and upper levels. The CV signal is generated by comparing the U_SERVO output from IC5A using IC14A and IC14B as the window comparators. In the same fashion, the CC signal uses the I_SERVO output from IC6A using the IC14C, IC14D comparators. The generated signals are level shifted for TTL inputs (using the R86, R89 and R98, R100 voltage dividers).

## Remote sense reverse polarity detection
Fig. 12: CC/CV indications, Remote sense reverse polarity detection
Remote voltage sensing is necessary to insure precise output voltage programming regardless of output current. It is essentially impossible to deliver power to a load with 1 mV precision, without remotely sensing the voltage at the load's input terminal, at the end of a cable a meter or three away from the PSU's output terminals. Output currents of a few amperes through insufficiently robust connection cables, or to load terminals with a resistance in miliohms, could easily produce a voltage drop across the cable from a few milivolts to even a few hundred milivolts. When using remote sensing, the output voltage actually supplied to the load is not measured at the power supply’s outputs but at the connected load terminals. The CV control loop (i.e. the error amplifier and correction circuitry) can compare that voltage against the programmed one, and all the voltage drops along the cable will have no effect. The technique is generally referred to as “Kelvin sensing” or 4-wire measurement technique.

Exposing the voltage sensing inputs to some external connection has disadvantages, however. The major one, not always obviously, is that any or both of sense inputs can be mistakenly connected in a reverse polarity fashion. This is likely to cause troubles. Internally, local sensing will be correct because the the signal relay on the Arduino Shield board will insure the correct connection (i.e. Sense+ to Out+, and Sense– to Out–).

When remote inputs are disconnected from the load input power connectors (via mistake, someone tripping over a cable, failure of an alligator clip to live up to its namesake's grip, …), the PSU can still work safely because they are still properly polarized thanks to R32, R59 with only a small deviation in output voltage because their additional 2 x 2 kΩ are added to the input voltage divider of IC5B.

If a sense input wire is connected to the opposite polarity power output, there will be a serious fault condition, for the input signal will have no relation to the channel attempting to ensure correct voltage and current to the load. There will be a maximum error bias within the CV control loop; it will try to compensate, and the end result will be the maximum possible voltage on the output. As one may imagine, this could easily result in irreparable damage to the connected load.

To avoid some of these unfortunate events, a reverse polarity detection circuit (Q18, Q20) has been added in parallel with the remote sensing inputs. It has two purposes: first, to immediately decrease output voltage to under approx. 1.7 V (Q17), and to generate a SENSE_ERR signal (Q19) that will notify MCU to immediately disable output.

Regardless, it’s still a very good practice to limit output current to a load to only a small current above that expected by the device when it's in normal operation. If there is no understanding of what the circuit should normally draw, it's time for more thought and analysis of the circuit, not time to power it up. The magic smoke might get out.
## PCB layout
The PCB layout shown in Fig. 13 includes all the mandatory and optional parts from the circuits discussed. Both DC and AC power inputs options are supported. The two layer PCB (laid out with Eagle, but without the autorouter) puts many limitations on arranging this fairly complex design in such a limited space. One goal was to to house everything in an enclosure no higher then the 2U (89 mm) form factor. Another limitation is to provide sufficient cooling for the power SMD components (i.e. Q1, D1, L2, but also IC1, Q5, Q14, R65) and the main THT power component (Q4).
The vertical orientation of the two Power board PCBs facing each other was chosen to create a kind of flow tunnel when the top and bottom enclosure plates are installed – this is the intended operational condition and the PSU shouldn't operated with them. The ∅60 mm cooling fan should be located on the one end of the tunnel structure while on the opposite end both Power boards are connected to the Arduino shield. Both top and bottom enclosure plates require multiple ventilation slots to ensure good air flow, and to cope with the possibility that either top or bottom holes might be blocked in some way.

Fig. 13: PCB layout r5B12 (both sides)
The height of the Power PCB is 74 mm which allows us to mount it in an 80 mm enclosure. They are screwed to an U-profile heatsink (custom made by Varisom) which is fixed on the enclosure top and bottom plate.

The PCB’s top side is oriented toward the tunnel interior to maximize air flow over the SMD components. Due to their size some THT components: X1, L1 (DC input) and X19, C144, C146 (AC input) are mounted on the bottom side of the PCB.

For the same reason Q4 (Fig. 14) and its heatsink are also mounted on the bottom side. Four 3.2 mm holes are provided to mount the PCB to the heatsink using 5 mm spacers. Additionally, cooling of the critical SMD components can be further improved by putting a “thermal bridge” between the bottom side of the PCB and the Q4 heatsink. A 5 mm thick conductive silicone thermal pad is highly recommended.

Fig. 14: Q4 power MOSFET position (PCB r5B12)
The PCB layout uses a single ground plane that occupies most of the bottom side. Components that belong to the power pre-regulator, bias pre-regulator, and analog and digital circuits are strategically grouped together and separated from other circuitry to decrease interference. This Power board is a great candidate for a 4-layer PCB which could provide better ground plane coverage, and so reduced EMI output. A future version may be a multiple layer board.

The ground plane has several sections. All of them are connected together below the power pre-regulator’s output capacitor (C15). IC1’s analog ground, on the top side, is connected with separate line (SH2) to the C15.

Outgoing positive and negative power lines are place in close proximity to each other to keep line inductance low. They also have exposed solder masks so that additional solder can be manually added if necessary. They are 150 mils wide which should be enough for 6.3 A of output with temperature rise of 10 oC for the 35 μm thick cooper traces.

The precision voltage reference is located close to the PCB edge (which is intended to decrease fluctuations possibly induced by mechanical vibrations); it is relatively far from the main sources of heat (IC3, Q1, D1, L2, L3, L4).

The R65 high current current sense resistor is an ordinary two-terminal 2512 resistor, therefore the Kelvin connection (i.e. 4 wires) must be established by a careful arrangement of the high current, and low voltage traces.

## SPICE models
(add links here)