# Firmware
Current version	v1.02
Status	Completed, ready for production
Supported HW	EEZ PSU H24005 (Arduino Shield r3B4 or newer)
Simulator	Windows, Linux, OS X
File repository	https://github.com/eez-open/psu-firmware
License	GNU GPLv3
Contributions	C4.1 (Collective Code Construction Contract)

The PSU firmware program is an Arduino sketch that must be uploaded to the Arduino board connected to the Arduino shield module. Instructions about firmware downloading, compiling and uploading can be found here.

The firmware sketch was tested with the Arduino IDE 1.8.2 and requires three additional libraries that come with the source code distribution. When they are properly installed you should see them in the Arduino IDE as shown on the picture below.

Please download and install Ethernet2 and SCPI parser directly if Arduino IDE reports errors during compilation.

## Software simulator
Fig. 1: Installed additional Arduino libraries
A unique feature of the firmware is the capability of running it without the underlying hardware. There is a software simulator (described in Section 9 of the SCPI reference guide). Another important firmware feature still rare (or almost non-existent) within the DIY/open hardware community is comprehensive support for SCPI. The SCPI represents the core of the firmware; it allows remote control of the bench power supply using various application suites designed for instrument control. For example, one can use the Keysight Command Expert freeware for the bench power supply control and monitoring.
## Memory usage
Arduino Due
Sketch uses 415712 bytes (79%) of program storage space. Maximum is 524288 bytes.
## Main page overview

Fig. 2: Main page default view items
Item	Description
Event viewer	Event viewer displays list of up to 100 recently recorded events about PSU activity like changing channel's output states, detected errors, self test errors, entering standby mode, etc.
AUX temperature sensor	AUX temperature sensor protection settings and state indication (Yellow – not defined/disabled, Green – enabled, Red – tripped). See also SYSTem:TEMPerature:PROTection[:HIGH][:LEVel]
Serial (USB) communication	Serial communication settings and indicator (Not visible – disabled, Yellow – enabled, Green – communication established). See also SYSTem:COMMunicate:SERial:BAUD
Ethernet communication	Serial communication settings and indicator (Not visible – disabled, Yellow – enabled, Green – communication established, Red – communication error). See also SYSTem:COMMunicate:ETHernet:ADDRess
INHibit pin state	Digital input pin INHibit state indicator (Not visible – undefined, White – defined, Red – activated). When PSU is in inhibited state all outputs are disabled and execution of LIST on channels is stopped. See also [SOURce:]DIGital:PIN<n>:FUNCtion
CH1 / CH2 LIST step countdown	Channel output programming LIST duration (DWELl) time countdown. Visible only for duration of 5 or more seconds formatted as hours/minutes, minutes/seconds or just seconds. See also [SOURce[<n>]]:LIST:DWELl
Main page appearance	Change main page appearance from numeric (default view, Fig. 2) to bar-graph horizontal, bar-graph vertical or YT-view (Fig. 3). See also DISPlay:VIEW
Channel ON/OFF or measured value	Use this area to enable (ON) or disable (OFF) channel output. When default appearance is selected measured output voltage is displayed when channel is in constant current (CC) mode or measured output current when channel is in constant voltage (CV) mode. If unregulated (UR) mode is detected, this value will be painted red. See also OUTPut[:STATe] and OUTPut:MODE?
Channel Low-ripple mode	Low ripple mode settings and indicator (Yellow – not active, Green – active). See also [SOURce[<n>]]:LRIPple
Channel Over-current protection	Over-current protection (and limit) settings and indicator (Yellow – not defined, Green – enabled, Red – tripped). See also [SOURce[<n>]]:CURRent:PROTection:STATe
Channel Over-voltage protection	Over-voltage protection (and limit) settings and indicator (Yellow – not defined, Green – enabled, Red – tripped). See also [SOURce[<n>]]:VOLTage:PROTection:STATe
Channel Over-temperature protection	Over-temperature protection (and limit) settings and indicator (Yellow – not defined, Green – enabled, Red – tripped). See also SYSTem:TEMPerature:PROTection[:HIGH][:LEVel]
Channel Over-power protection	Over-power protection (and limit) settings and indicator (Yellow – not defined, Green – enabled, Red – tripped). See also [SOURce[<n>]]:POWer:PROTection:STATe
Channel set voltage	Output voltage settings. See also [SOURce[<n>]]:VOLTage
Channel set current	Output current settings. See also [SOURce[<n>]]:CURRent
System settings	System settings provided on two pages: / Page (1): AUX temperature sensor, System protection, Trigger, Digital I/O, Date and time, Encoder / Page (2): Serial (USB), Ethernet, Channel calibration, Display, Sound, System password
User profiles	User profile settings. See also *SAV, MEMory:STATe:CATalog
Channel settings	Channels settings: Protections, Trigger, Advanced, Information. When channels are in tracking mode or coupled in series or parallel, only one Settings option will be available and values for both channels will be presented on Information page.
System information	System information provided on two pages: / Page (1): total on time, last on time, measured temperature on AUX sensor, fan speed, firmware version, serial number / Page (2): CPU board (Arduino Shield) revision, Ethernet controller, CH1/CH2 Power boards revisions, SCPI version
Display lock	Lock/unlock local display. To unlock system password will be required if defined. See also SYSTem:KLOCk and SYSTem:PASSword:NEW
Main page help	Main page basic help
Standby, Display off, Soft reset	Shows menu with options for entering Standby mode (SYSTem:POWer), switching TFT local display off (DISPlay[:WINdow][:STATe]) or perform soft reset (*RST). / If Standby mode is entered, you have to tap anywhere on the screen and hold it for few seconds for powering the PSU back.

## Roadmap
Fig. 3: Other Main page appearances
Version	Description	Release time frame
M1 (Milestone one)	SCPI compliant firmware for the power supply as an SCPI device class that includes programming of voltage, current, OVP (over-voltage protection), OCP (over-current protection), OPP (over-power protection) and OTP (over-temperature protection), output measurement, ADC/DAC voltage and current calibration, output control, remote sense control, power up control, system date/time (using RTC), diagnostic reporting, beeper, Ethernet and serial (via USB) communication. It also include support for complex SCPI status registers structure.	12/2015
M2	Adds support for a local console (within the PSU) based on a color TFT touch screen display as an input device that removes the requirement for many buttons and switches on the front panel. It also enables better user interaction thanks to use of a “pointing device” (i.e. your finger on the touch-screen) that commercial devices in general still do not offer. / Both portrait and landscape TFT display orientation will be supported and display pages will be generated using the EEZ Studio visual toolkit.	10/2016
M3	Channel coupling (parallel, series) with balancing, channel tracking, AUX temperature sensor OTP settings, fan speed control, negative power monitoring (power sink) for down-programmer protection, system lock/password management.	12/2016
M4	Encoder support, “YT view” for displaying output values, arbitrary waveform generator, triggers, initial SD card support.	03/2017
M5	Dual channel current range, a first time installation wizard, improved output value precision.	05/2017
v1.0	Digital I/O support, Ethernet settings, serial port settings, support for NTP (real-time clock synchronization).	06/2017
v1.01	Calibration bug fix for older Power board’s (r5B9). The native USB port is set as default one. A few minor improvements.	07/2017
v1.02	Few minor fixes	10/2017
v1.1	SD card file management, Data logging. See also GitHub Milestones section.	?

## Downloads
{jd_file file==1}
{jd_file file==2}