# Firmware
Current version	M4 (Milestone Four)
Status	Completed, ready for production
Supported HW	EEZ PSU H24005 (Arduino Shield r1B9 or newer)
Simulator	Windows, Linux, OS X
File repository	https://github.com/eez-open/psu-firmware
License	GNU GPLv3
Contributions	C4.1 (Collective Code Construction Contract)

The PSU firmware is an Arduino sketch that has to be uploaded to the Arduino board that is connected on to Arduino shield module. Instructions about firmware downloading, compiling and uploading can be found here.
The firmware sketch is tested with Arduino IDE 1.6.13 and require five additional libraries that comes with the source code distribution. When they are properly installed you should see them in the Arduino IDE as shown on the picture below.

## Software simulator
Fig. 1: Installed additional Arduino libraries
Unique feature of the firmware is possibility to run it without any underlying hardware thanks to software simulator that is described in Section 9 of the SCPI reference guide. Another important firmware feature that is still rare (or almost non-existent) within DIY/open hardware community is comprehensive support for the SCPI. The SCPI represent the core of the firmware and it allows remote control of the bench power supply using various application suites designed for instruments control. For example one can use the Keysight Command Expert freeware for the bench power supply control and monitoring.
## Memory usage
Due
Sketch uses 341,456 bytes (65%) of program storage space. Maximum is 524,288 bytes.
## Roadmap
Version	Description	Release time frame
M1 (Milestone one)	SCPI compliant firmware for the power supply as a class of device that include programming voltage, current, OVP (over-voltage protection), OCP (over-current protection), OPP (over-power protection) and OTP (over-temperature protection), output measurement, ADC/DAC voltage and current calibration, output control, remote sense control, power up control, system date/time (using RTC), diagnostic reporting, beeper, Ethernet and serial (via USB) communication. That also include support for complex SCPI status registers structure.	12/2015
M2	Add support for local console based on color TFT display with touch screen as an input device that remove requirement for many buttons and switches on the front panel and in parallel enables better user interaction thanks to “pointing device” (your finger on the touch-screen) that commercial devices in general still do not offer. / Both portrait and landscape TFT display orientation will be supported and display pages will be generated using the EEZ Studio visual toolkit.	10/2016
M3	Channel coupling (parallel, series) with balancing, channel tracking, AUX temperature sensor OTP settings, display fan speed, negative power monitoring (power sink) for down-programmer protection, system lock/password management.	12/2016
M4	Encoder support, “YT view” for displaying output values, Arbitrary waveform generator, triggers, initial SD card support.	03/2017
M5	Dual channel current range, first time installation wizard, improved output values precision.	Q2/2017
v1.0	Digital I/O support, Ethernet settings, serial port settings, support NTP for real-time clock synchronization.	Q2/2017
?	SD card file management, Data logging, support for *SRQ (service request) over Ethernet, etc. See also GitHub Milestones section.	?

## Downloads
(add links here)